## Slide 1: Chapter 4
Digital Image Fundamentals

## Slide 2: Need for Image Processing
Improvement of Pictorial Information for Human Perception
  Noise Filtering
  Contrast Enhancement
  Deblurring etc.
Image Processing for Autonomous Machine Application
  Industrial Machine Vision for Product assembly and inspection
  Automated Target detection and tracking
  Finger Print Recognition
  Machine Processing of satellite and aerial imagery
  Video Sequence Processing ( Movement Detection)
Efficient storage/ transmission
  Image Compression

## Slide 3: Image Representation in Digital Computer
  Image is a 2D light intensity function f(x,y)
  A digital image f(x,y) is discretised both in spatial coordinates and brightness.
  Can be considered as a matrix whose row and column specify a point in the image and element value specifies gray level value at that point
  These elements are referred to as pixels.

## Slide 4: Image Representation in Digital Computer

## Slide 5: Sampling and Quantization
  Spatial discretization by Grids
  Intensity discretization by Quantization

## Slide 6: Sampling and Quantization
  Spatial discretization by Grids ( Sampling)
  Instead of storing all the intensity values of all possible points in the image we try to take samples of the image on a regular grid.
  The grid is superimposed on this particular image and what we do is we take samples, image samples at various grid points.
  Typically for image processing applications, the image size which is used is either 256 x 256 elements, 512 x 512 elements, 1 K x 1 K elements and so on.
  Intensity discretization by Quantization
  After sampling, at every point the value of that particular sample is again continuous. So it can assume any of the infinite possible values, which again cannot be represented in a digital computer.
  Quantization is done using 8 bits for black and white image and using 24 bits for color image ( RGB planes).

## Slide 7: Desired Output after sampling and quantization
  Image should be represented in a form of finite two dimensional matrix like this. So this is a matrix representation of an image and this matrix has got finite number of elements.

## Slide 8: Image Digitization
  Image Digitization= Sampling + Quantization

## Slide 9: Image Digitization

## Slide 10: Types of Images

## Slide 11: Image Digitization

## Slide 12: Advantage of Digitization
Storage and retrieval of digital images are faster as well as cheaper than analog images.
Digital images allow compression (size reduction) using a variety of methods.
We can segment a digital image by detecting discontinuities such as points, lines, and edges.

## Slide 13: Relationship between Pixels
  Neighbourhood of Pixels
    4 Neighbourhood

## Slide 14: Relationship between Pixels
  Neighbourhood of Pixels
    Diagonal Neighbourhood

## Slide 15: Relationship between Pixels
  Neighbourhood of Pixels
    8 Neighbourhood

## Slide 16: Connectivity
It is used for establishing boundaries of objects and components of regions in an image.

## Slide 17: Connectivity

## Slide 18: Connectivity

## Slide 19: Connectivity

## Slide 20: Example for solving

## Slide 21: Example for solving

## Slide 22: Example for solving

## Slide 23: Example for solving

## Slide 24: Image File Formats
BMP ( Bit Mapped Graphic Image)
  Developed by Microsoft
  Can save both monochrome and colour image
  Very Good quality images
  Occupy lot of memory
  Eg- wall paper images, Image editing
TIFF ( Tagged Image File Format)
  Developed by ADOBE
  Large file size. Hence, Occupy lot of space.
  Very high Quality Images
  Because of large sizes, plugins are generally required to display them on internet sites
  May or may not be compressed (Uses Huffman coding and LZW algorithm for compression)
  Eg- OCR, HD imaging
JPEG ( Joint Photographic Expert Group)
  Compressed Images
  Occupy very little space
  Uses DCT for compression
  Lossy compression algorithm
  Quality is not good

## Slide 25: Distance Measures
Euclidean Distance- Given two points p (x,y) and q(s,t)
City Block Distance( Manhattan Distance): Given two points p (x,y) and q(s,t)
  (p , q)=
Chess Board Distance: Given two points p (x,y) and q(s,t)
          (p , q)= max(